## Slide 1
ORE
VISTA
AI-Powered Gold Stope Optimizer
From block model to ranked mine plan — in under 60 ms
148,500+
Stope candidates evaluated
< 60 ms
Full optimisation time
3,000 m³
Per stope volume
100 %
Hackathon spec compliant
Hanson Venture Lab Hackathon 2026

## Slide 2
The Problem
2
Underground gold mining hinges on one question every mine planner asks daily:
"Which blocks should we excavate - and in what order?"
⏳ Days of manual work
Engineers delineate stopes by hand in legacy CAD tools. A full mine plan takes days of specialist labour.
💸 Poor economic visibility
Cutoff grades are set by gut feel or static tables. The true NSV of each stope is rarely computed in real time.
📐 Spec compliance risk
WAG (Weighted Average Grade) must use per-block volume. Hardcoded cell sizes introduce silent calculation errors.
🔁 No live scenario testing
Changing the gold price or cutoff requires re-running the entire workflow — so it almost never happens.
2

## Slide 3
OreVista — Our Solution
3
One browser session replaces days of specialist mine planning software.
01
Upload
Drag-and-drop block model CSV
Auto-detects XINC/YINC/ZINC
Polars parser — 8× faster than pandas
02
Compute
Vectorised NumPy sliding window
148,500 stope candidates in <1 s
Binary .npy cache for instant reload
03
Optimise
1D dynamic programming per strip
Globally optimal non-overlapping set
Rust/Rayon: ~60 ms end-to-end
04
Explore
3D interactive stope viewer
Live NSV calculator (11 parameters)
Part 1 & Part 2 cutoff modes

## Slide 4
Technical Architecture
4
FRONTEND
React 18 + Vite
Three.js 3D viewer · Recharts · Tailwind
API
FastAPI + Uvicorn
10 endpoints · async · CORS · upload
ENGINE
NumPy + Polars
Vectorised sliding window · binary cache
ACCELERATOR
Rust + Rayon + PyO3
Parallel DP · ~60 ms · optional
Core Algorithms
Spec-Compliant WAG (Technical Notes §5)
WAG = Σ(Vᵢ × Dᵢ × Gᵢ) / Σ(Vᵢ × Dᵢ)
volume × density × grade / volume × density
Volume per block (Technical Notes §1–§2)
Vol = XINC × YINC × ZINC
(5 × 5 × 5 = 125 m³ for hackathon dataset)
Stope geometry
20 m (L) × 5 m (T) × 30 m (H) = 3,000 m³
4 × 1 × 6 blocks — fixed per spec
DP selector (per Y-strip per Z-level)
dp[i] = max(dp[i-1], dp[i-stope_len] + nsv[i])
→ globally optimal non-overlapping set O(n)

## Slide 5
Hackathon Compliance Checklist
5
Every requirement from the Technical Notes — addressed.
Technical Notes §
Requirement
Status
How We Meet It
§1–§2
Volume = XINC × YINC × ZINC per block
✅ Fixed
parser.py reads XINC/YINC/ZINC; per-block volume_grid
§3
WAG = Σ(V×D×G) / Σ(V×D)
✅ Done
optimizer.py uses vgd/vd with volume_grid
§4
Missing blocks: 0 g/t grade, 2.8 t/m³ density
✅ Done
fill_null defaults in parser.py
§5
Non-overlapping stope selection
✅ Done
1D DP per Y-strip per Z-level
Part 1
Fixed 10 g/t cutoff, ranked stope output
✅ Done
GET /api/optimize?cutoff=10
Part 2
Live cutoff slider, re-optimise in real time
✅ Done
Frontend slider → API → instant re-rank
Part 2
Speed test — full optimisation ≤ 2 s
✅ Done
Rust: ~60 ms · Python fallback: <1 s
Output
CSV export of ranked stopes
✅ Done
GET /api/export/csv
Bonus
Grade-tonnage curve
✅ Done
GET /api/grade-tonnage + Recharts UI
Bonus
NSV economic model (gold price, recovery, OPEX…)
✅ Done
11-parameter NSV in optimizer.py

## Slide 6
The Critical Fix: Per-Block Volume
6
❌ v1.0 — Original (Spec Violation)
# CELL_SIZE hardcoded — XINC/YINC/ZINC never read
CELL_SIZE = 5
VOL_PER_BLOCK = 125 # m³ — same for every block!
required = {"XC", "YC", "ZC", "AU", "DENSITY"}
# ^ XINC, YINC, ZINC missing from required!
# Returns 5-tuple — no volume_grid
return grade_grid, density_grid, x, y, z
✅ v2.0 — Fixed (Spec Compliant)
if {"XINC","YINC","ZINC"}.issubset(cols):
xinc = df["XINC"].fill_null(5.0).to_numpy()
yinc = df["YINC"].fill_null(5.0).to_numpy()
zinc = df["ZINC"].fill_null(5.0).to_numpy()
# Per-block volume — Technical Notes §2
block_vol = xinc * yinc * zinc
else:
cs = auto_detect_cell_size(xv, yv, zv)
block_vol = np.full(len(xv), cs**3)
# Returns 6-tuple with volume_grid
return grade, density, volume_grid, x, y, z
Impact: For the hackathon's uniform 5 m grid the numbers are identical. For any non-uniform block model, v1 was silently wrong — v2 is correct.

## Slide 7
Performance at Scale
7
~60 ms
Rust/Rayon full optimisation
< 1 s
Python NumPy fallback
148,500+
Stope candidates evaluated
8–10×
Faster CSV parsing vs pandas
Instant
Cache hit (binary .npy)
11 params
Live NSV economic model
CSV Upload
(Polars)
3D Grid
(NumPy)
Sliding Window
148K stopes
DP Selector
(Rust/Rayon)
Ranked
Results
⚡ Full pipeline — CSV in to ranked JSON out

## Slide 8
User Interface
8
🗺 3D Stope Viewer
Interactive Three.js scene
Colour-coded by WAG grade
Orbit · Pan · Zoom
Click any stope for full metrics
⚙ Parameter Panel
Gold price ($/oz)
Recovery, refining, smelting
Transport, royalty
Sustaining OPEX · Dev cost
📋 Report Table
Sortable ranked stope list
WAG · Tonnes · Gold oz
NSV per stope
CSV export one-click
📈 Grade-Tonnage Curve
Pre-computed 0–50 g/t sweep
Recharts line chart
Instant sensitivity view
Both Part 1 & Part 2 modes

## Slide 9
API Endpoints
9
FastAPI backend — fully RESTful, auto-documented at /docs
GET
/health
Liveness check — returns {status: ok}
GET
/api/model-info
Grid dimensions, block count, cell size
GET
/api/optimize
Run optimisation at ?cutoff=10 (or any g/t)
GET
/api/grade-tonnage
Grade-tonnage curve — 0 to 50 g/t sweep
GET
/api/export/csv
Download ranked stopes as CSV
GET
/api/report
Summary stats JSON (ore, waste, NSV total)
POST
/api/upload
Upload new block model CSV (multipart/form-data)
POST
/api/preload
Pre-warm binary cache from server-side path

## Slide 10
Why OreVista Wins
10
🎯
Correct
Per-block volume from XINC×YINC×ZINC
WAG = Σ(V×D×G) / Σ(V×D) — exact spec
Non-overlapping DP — no double counting
Missing block defaults per §4
⚡
Fast
Rust/Rayon parallel: ~60 ms
NumPy vectorised: <1 s
Binary cache: instant reload
Polars: 8× faster CSV parsing
🖥
Usable
Drag-and-drop CSV upload
Live cutoff slider — instant re-rank
3D ore body visualisation
One-click CSV export
🏗
Complete
Part 1 + Part 2 both implemented
Grade-tonnage curve
11-parameter NSV model
Full REST API with auto-docs

## Slide 11
ORE
VISTA
Block Model → Mine Plan → Under 60 ms
GitHub Repository
github.com/vvina-ten/OreVista
FastAPI · React · Three.js · Rust/Rayon · Polars · NumPy
✅ Fully spec-compliant WAG formula
✅ XINC × YINC × ZINC volume — fixed
✅ Part 1 + Part 2 complete
✅ ~60 ms Rust-accelerated pipeline
✅ Interactive 3D web interface
Hanson Venture Lab Hackathon 2026